## Slide 1
Slow Scan TV – ZiaCon 2024
CATMEMES
OVERHAMRADIO

## Slide 2
INTRO
I’m hamster
KD5WGW
electronics and ham radio nerd
yes I’m glad cookie season is over

## Slide 3
WHAT IS SSTV
Slow Scan TV is a collection of various encoding methods used to convert an image into a sound that can be transmitted and reconstructed at a distance
A single 320x256 image takes about 110 seconds to transmit, so this is not ‘live’ TV (aka Fast Scan TV) – just images

## Slide 4
SSTV DEVELOPMENT
1957
COPTHORNE MACDONALD
Invented the first algorithm
1960s
SPACE IMAGES
USSR and NASA used forms of SSTV to beam back images
1968
LEGALIZED FOR HAMS
FCC allows ‘advanced’ class amateurs to broadcast SSTV
1990s
SOFTWARE DEVELOPED
Home PCs began to get software to encode/decode

## Slide 5
EARLY SSTV
Specialized hardware called a Vidicon tube was required to encode an image
Original was 120 lines, 120 pixels per line

## Slide 6
PERSISTENCE OF VISION
Early SSTV took advantage of the properties of CRT screens to display images. ‘Storage’ was via film cameras
DIGITAL STORAGE
As PCs became available, images could be decoded and saved via digital means

## Slide 7
MODERN SSTV
Many free software packages exist to encode and decode SSTV
You can even encode and decode using your phone

## Slide 8
SSTV USAGE
FIRST IMAGES
SPACE
APOLLO
COMMERCIAL
1958
Work was improved by hams over a 10 year period
1959
Russian Luna 3 first images of the far side of the moon
1960s
NASA makes use of SSTV in space missions
EARLY 1980s
Robot Research Corp develops commercial units

## Slide 9
SSTV USAGE
AMIGA
IBM PC
POP CULTURE
PHONE
1990
Interface developed for Amiga computers - AVT
1990s
Improved sound cards allow for software decoding
2007
Valve uses hidden SSTV audio in game
2010s
Phone applications become available for SSTV on the go

## Slide 10
‘Fast Scan TV’ (broadcast television) is 3Mhz for black and white television or 6Mhz for color television
Total bandwidth for SSTV images is around 3khz
The first trans-Atlantic image
SSTV TECHNICALS

## Slide 11
ANALOG SIGNAL
SSTV uses frequency modulation to encode brightness levels – higher frequencies are lighter, and lower are darker
SSTV MODULATION
COLOR ENCODING
For color modes, each line is sent three times, for the Red, Green, Blue elements.
Some schemes send YCrCb instead, which is chroma values for RGB
TIMING AND SYNC
Each line has a specific timing, with a sync tone either in the middle or end of the line

## Slide 12
TRANSMISSION COMPONENTS
HEADER
  A calibration header starts a message
  A Vertical Interval Signaling (VIS) code in the header identifies the encoding type
SCANLINE
  Each line of the image is sent sequentially, ordered from left to right
  A sync pulse is at the end or middle of each line depending on mode

## Slide 13
SSTV TEST
SOURCE

## Slide 14
HEADER
The header starts with two 1900hz tones that are 300ms long with a 10ms break
Following that, there are 8 bits, with a start and stop bit. Bit 8 is a parity bit
This VIS code identifies what format the image is going to be transmitted in
This is typical of most modes in current use

## Slide 15
Scan lines encode the image information for each line as a function of the received frequency
At the end of each line, a sync pulse of 1200hz is sent
Some modes put the sync pulse in the middle of the scanline instead
Color images send three scan lines per actual scan line to encode the RGB value of the line
Very early color images were actually multiple black and white images, each with a color filter on the camera – a very manual process
SCAN LINES

## Slide 16
Paul Turner / Don Rotier
YCrCb color
Reduced xmit time
800x600 – 5 minutes
MODES IN BRIEF
PD
Martin Emmerson G3OQD
Improved on Robot Up to 320x256
Simplified color sync
Stations are synced
Martin
Robot Research Corp
YCrCb instead of RGB
Compat with B&W
Async transfer
Sync pulses can be lost
Robot
Improved on Martin
Same image quality
Adds a DX mode
Most popular in NA
Scottie
Eddie Murphy GM3SBC

## Slide 17
OTHER MODES
Tons of experimental/abandoned modes
MSCAN TV
Interlaced transmission
Kenwood FAST FM
Like Robot, but with odd parity
Built-in to some handsets
MP, MR, ML
VIS code extended to 16 bits
Sync is narrowband
Martin HQ
YCrCb encoding
Full specification never detailed
Many more!

## Slide 18
COMPUTER
A computer with a sound card, or even a phone
SOFTWARE
Many programs to choose from. MMSSTV is a good choice for Windows, or Robot36 for Android
SSTV SIGNALS
Record over the air, or use one of many online SDR radios to tune in
RECEIVING SSTV

## Slide 19
Hams like to use specific frequencies for SSTV traffic
80 meters – 3.845Mhz
40 meters – 7.171Mhz
20 meters – 14.230Mhz
15 meters – 21.340Mhz
10 meters – 28.680
TYPICAL SSTV FREQUENCIES

## Slide 20
TRANSMITTING SSTV
LICENSE
Any license will grant some bands, but you’re going to want to upgrade to General or Extra to use the lower bands
POWER
You can transmit at as high of a power as allowed for the band, but be mindful of causing interference
IDENTIFICATION
When transmitting SSTV, most hams will overlay their callsign on the image being transmitted. Some programs will template this for you

## Slide 21
EXAMPLES

## Slide 22
WHY TRANSMIT?
CONNECT
A fun way to connect without needing to use voice
Try new methods or modes
Improve upon current ones
Create unique images
Share your current view
INNOVATE
CREATE

## Slide 23
CHALLENGES AND LIMITATIONS
Transferring images is slow and can take considerable time
High power transmission can put considerable heat load on your radio equipment
Even with error correction, images can arrive out of sync or with significant artifacts
Higher license classes needed to access all of the bands
Much of the PC software is ancient, but functional

## Slide 24
FUTURE FUN

## Slide 25
AN SSTV BADGE?
Of course I’m going to make this into a badge
LCD screen
Microphone
Microcontroller
Hopeful to have a prototype this month
Attempting to do all decoding on the chip without resorting to a Raspberry Pi

## Slide 26
QUESTIONS?