## Slide 1: Intro to Logic Analyzers
hamster
SAINTCON25

## Slide 2: Howdy
I’m hamster

## Slide 3: BACKGROUND 01

## Slide 4: What is logic?
Logic is digital data – ones and zeros
Logic defines timing of pulses

## Slide 5: What is not logic?
Logic does not define voltage levels
Logic does not show rise and fall times

## Slide 6: What is a logic analyzer?
A logic analyzer is a device that captures logic data
Logic analyzer software can usually also decode the raw data into ‘human’ readable bytes

## Slide 7: What about an oscilloscope?
An oscilloscope displays voltage with respect to time
An oscilloscope will likely not decode the data
Some oscilloscopes have built-in logic analyzers

## Slide 8: What one to choose?
Oscilloscope
- Shows what is actually on the wire
- Can see rise and fall times, voltage levels, and noise
- Pick a scope when you need low level troubleshooting

## Slide 9: What one to choose?
Logic Analyzer
- Shows a representation of data
- Can decode data streams
- Pick this when you need to decode/debug a data stream

## Slide 10: PICKING A LOGIC ANALYZER 02

## Slide 11: What are the features?
Channels
Speed
Buffer
Software
Cost

## Slide 12: Channels
Channels are captured in parallel to compare multiple signals
Multiple channels are needed for some protocols
I2C – 2 channel
SPI – 3+ channels
Parallel – 8+ channels

## Slide 13: Speed
Sample rate is important to capture all the data
Nyquist-Shannon sampling theorem states that the sample rate must be at least twice the captured signal in order to avoid aliasing
Aliasing basically means you miss edges because they happen while you are not looking

## Slide 14: Buffer
Buffers store data on the analyzer in real-time so they can be streamed later to a PC
Larger buffers allow more sampling time before needing to ‘come up for air’ and transfer the data back to the host

## Slide 15: Software
Some open-source software such as PulseView or sigrok exist and supports most logic analyzers
Vendor software is a grab bag of awful and awesome

## Slide 16: Cost
Standalone models can be very expensive
Better features add cost
Very cheap logic analyzers work for most casual users, however

## Slide 17: CHEAP LOGIC ANALYZERS 03

## Slide 18: Logic Analyzers on the Cheap
Saleae logic analyzers cost between $500-$1500
Some models have oscilloscope channels as well
Very good ‘cheap’ units
Software is very good
Very often older models are cloned

## Slide 19: Logic Analyzers on the Cheap
DreamSourceLab has models from $150-$400
Software is a closed source spin of PulseView (more or less)
A very good value for hobbyists who want something professional

## Slide 20: Logic Analyzers on the Cheap
Digilent Analog Discovery is about $380
Bonus with this unit is that it has a couple of oscilloscope channels as well
Software works pretty well

## Slide 21: Logic Analyzers on the Cheap
Chinese clones are $3-8 bucks depending on tariffs
Most clone Saleae Logic 8 analyzers and will work with Saleae software
Pretty reasonable for a pocket logic analyzer

## Slide 22: SETTING UP 04

## Slide 23: Circuit considerations
Make sure you know your voltage levels of the signal you want to connect to
Be careful you are not providing a ground path from an isolated, high voltage system through your computer
Any probe on a live circuit can affect how the circuit works or cause it to glitch or stop working

## Slide 24: Connecting
Probe clips are usually used
Connect with the device power off to prevent shorts
Make sure you always connect up a ground

## Slide 25: Setting up
Configure each channel type
You can rename channels

## Slide 26: Protocols
To decode a protocol, depending on the software, you add a decoder and use a popup to select what channel is what pin

## Slide 27: Triggering
Triggers can be set to start captures when a certain logical condition is met
Or you can just start a capture
Or you can run an auto-repeating capture

## Slide 28: RESULTS 05

## Slide 29: Example

## Slide 30: Example

## Slide 31: Example

## Slide 32: THANKS!
Do you have any questions?
Mastodon @hamster@fosstodon.org
bsky @hamster.dczia.net
Twitter @hamster
Discord @pcbhamster
Srsly that’s too many